AN1

SAGA OF '71 V-4 BATTERY, REGULATOR, ALTERNATOR

After returning from the Flea Market Sept 2, I could not restart the V-4, the battery was too low, barely enough amps to click the starter motor. A jump start by a friendly Bob Golden a mechanic across the alley proved wiring and engine were OK. Bob used his Snap-On electronic box to test the regulator, etc. The palm size box has 5 lights which can tell if the battery is low or charged, the regulator is malfunctioning or a combination of faults.

Bob advised me to have the alternator checked out, after I buy a new battery and a new regulator (Harting, BO-13-0102, 1/14V 087, 177-0015 Beck Arnley). He also informed me of a good alternator-starter motor rebuild shop nearby: S & M Auto Electric, at the rear of 2611 W. Peterson,Chicago (728-4405).

The alternator man removed the alternator and placed it on the test machine. It could only put out 20 AMPS instead of the normal 40 AMPS for a subcompact car. He tried to select a couple of Bosch rebuilts he had in stock but the housing/casting would not fit our SAAB bracket. So he disassembled the entire alternator-tested and showed me that at least one diode was blanked out. Also, the pulley bearing was noisy. He masked, sand blasted, painted, and replaced diodes, bearing, brushes, turned downed the copper slip rings. Back on the test machine showed a 34 AMP charging ability. He did not have a suitable rewound field coil available, which his normal rebuilt unit would include. All this took 2-1/2 hours while I waited and observed, price; under $70.00.

You cannot test the alternator while on the car, and no dealer can test and rebuild the alternator. Take it to an alternator/generator repair shop.