AN10

SONETT DECELERATION VALVE FIX

PLUS FUEL ALTERNATIVE

The engine nearly stalled when I covered the bleed hole in the bottom cover of the valve. I went to the local SAAB dealer and picked up a new diaphragm (#88-49-259) and paid $13.65. After talking to a friend of mine who also owns a '74 Sonett, he concluded his diaphragm was also bad. Realizing we have a Ford engine, he went shopping at the local Ford dealer. He found an identical diaphragm (Motorcraft P/N CM-2204) for only $4.88. It is used on the Pinto 1600 cc engine. He found there is also one available for $5.60 at the Mercury dealer, used on the '70-'71 Capri engine.

A couple of weeks ago, my fuel pump started spewing oil all over the side of the engine and engine compartment. The problem turned out to be merely a torn boot on the pump push shaft. I found a nearly identical fuel pump at the local Mercury dealer. The only difference being that the inlet connection was at a slightly different angle than the original. It also did not have the rubber boot which failed on the original. The position of the inlet connection is determined only by orientation of the cover and it orientation was predetermined by a dimple in the cover and a matching dimple in the body of the pump. By merely bending out the dimple on the rim or the cover, the cover can be rotated to bring the inlet connection into the same position as it was on the original. The pump I bought (#D3FZ A RM) was a rebuilt pump and cost $27.90. A new pump (#D4R4) would of cost $31.30.