AN101

CARB DECEL VALVE LEAKS

The engine in my V-4 developed a curious malfunction pattern. After starting the engine, it would run fast for a brief interval, then stall, and abruptly choke itself out. I proceeded to perform the following:

1. Check for sustained fuel and pump pressure to the carb.

2. Perform several carb adjustments, including opening and closing the air mixture and idling screws.

3. Examine the hose between the carb and decel valve for possible air escaping.

4. Removed the carb and replaced a deteriorated acceleration pump diaphragm and selected other suspicious parts.

5. Inspected the decel unit and found the diaphragm in bad condition and replaced it. (You can use the diaphragm from a Ford Pinto, P/N D1FZ-9K799-B from Ford)

6. Removed, examined and cleaned the PVC valve.

7. Checked for a hose air leak between the distributor vacuum chamber and the carb air horn.

8. Removed the distributor cap and examined the rotor and the points.

After performing all of the above diagnostic steps I started the engine only to learn that nothing was achieved. In a subsequent attempt to isolate the problem, I removed the 1/2" hose which connects the decel valve to the vacuum drum on the power brake unit. I filled this hose with water and observed for a possible leak. None. Then placing the hose to my mouth and sealing the other end with my thumb, I blew hard. Eureka! Air escaped from the elbow joint which connects to the decel valve outlet where a defective clamp had damaged the hose. In replacing the hose I carefully tighten the clamps to avoid scarring or piercing the rubber, and after that the engine has performed beautifully.