AN102

WATER PUMP REMOVAL

Changing the water pump on a 96 is awful. In addition to the instructions in the newsletter, July 1978. I can only add that to make it easier the next time , remove the three bolts nearest the engine and drill the threads on the water pump, and replace the three bolts with 1/4" bolts and put nuts on the front. Then the next time you will not have to remove all those hoses and the motor mount. This can also be done when the engine is out of the car for other reasons.