AN108

WIPER MOTOR LEAKS SONETT

Any Sonett owner who has the hood off should check the windshield wiper motor for internal rust. The manufacturer provided a hole on the top for water to enter (wiring hole) but no drain hole holes in the lower casing. Mine was rusted, but salvageable. i drilled two drain holes, used silicone around the wiring, and the motor works like new. The brush assembly for a '71 or newer is Lucas P/N 54701528, available from a SAAB dealer.

Ed Note: tips on rusting Sonett wiper motors have appeared in the Newsletter before, but since it can be a very serious failure in certain circumstances, repeating it should be helpful. Getting the brush assembly and rebuilding the motor is also a good idea, as that is usually a;; that is wrong, and people often give up on an old motor that could be rebuilt.