AN11

SONETT III EXPERIANCES ON NOISE REDUCTION,

WIPER MOTOR REPAIR PLUS CLUTCH SUGGESTIONS

The Sonett tends to be a noisy little car, what with exhaust boom, lack of insulation and fiberglass body. A significant reduction in the interior sound levl can be realized through judicious application of jute and insulation material. The jute can be cut to go under all carpet panels and to line the spare wheel well. Buy a roll of ordinary house insualtion (4" thick) and push it into every body cavity you can find...you'd be surprised how many there are, and all empty.

Remove the seats, lift up the upholstery in front of the gas tank and you'll see lots of openin space; same with  behind it. Unsrew the rear quarter panel upholstery peiced and stuff the places you find there. Other places: above the carpeting and inside the firewall, inside the forward kick panels on both sides, on the underside of thne hood, especially on the engine side of the firewall, inside the doors (be careful not to interfer with the windows or winding mechanism) and inside the gearshift linkage tunnel. Also liberal usage of spray-on undercaosting will deaden road noise (apply this only after you have scrapped away the rust and primed the surfaces of bare metal), even though it (spray-on undercoat) does virtually nothing to prevent underbody corrosion.

Just replaced my windshield wiper motor motor with a rebuild from Performance Cars ($50.00 with exchange). They have a new twist to prevent the motor housing filling up with water (something all long time Sonett owners are overly familar with): They drill two holes in the "bottom" of the housing to allow water to drain out of. This can be done to the motor while installed in the car, with a little patience. Be sure to seal the two openings in the top with silicone. Pull out and throw away the tar SAAB presses into the hole the wires enter. If you have the motor out, closely examine the cable where it runs through the two spindles (or wheel boxes, depending upon who you're talking to): if it shows the slightest wear or flattening (inevitable after 50,000 miles and moderate use), replace it. Else, the cable starts to slip on the spindle gear, causing a horrendous sound and inevitable failure.

My wipers stopped parking automatically, too. Found that corrosion had gotten to the very fine winding wire which runs to the terminal junction inside the wiper relay case. Splice in a new 1" length, solder in place, replace the cover, silicone all around the edge where the cover goes and presto, they work again. Same story inside the headlight relay case (as someonbody recently reported in the newsletter) if the headlight start flickering on and off or go off completely and the fuses are not corroded.

I've put in three clutches now (my Sonett has 80,000 miles); finally learned my lesson the third time around and replaced the pressure plate springs with heavy duty red ones (stock are blue) from Raymond Merchandise, Barnes Group, 380 Scoita St. Corry, Pa. 16407. Ask for there P/N 120-416-132 RED. Don't know the price, as salesperson I spoke with sent me a set at no-charge samples. They make them for a couple of customers, in quanity, so may not have them in stock; in that case, find out who buys them. The clutch should go 100,000 miles, with these springs 25,000 with the stock springs. Also, don't buy a new disc-have the old one re-faced with a better compostion material (which will probably be thicker tahn stock SAAB). Incidentally, VW sells a throwout bearing identcal to SAAB's for 1/3 the price.