AN111

CLUTCH ADJUSTMENT TOOL

When replacing the clutch or experiencing shifting problems or clutch free play adjustment problems, check the adjustment screw. The new ones presently available from SAAB are a few mm's longer than most of the ones that I have found on V-4's. I have installed new clutches and then not been able to get the proper free play until I installed on of these replacement screws. It saves having to jury rig the slave cylinder with shims. One of these new screws is 31mm long compared to the 28mm I found on my car. The screw is P/N 88-095-50; your old lock nut will work.