AN112

BRAKES

The Capri brake master cylinder rebuild kit mentioned as fitting a '71 on V-4 (P/N D7RY-2004A) contains only seals. It doesn't contain the white plastic guide bushing that usually has to be drilled out in order to disassemble the cylinder, nor does it contain seal guides and washers, not to mention the pistons that the ATE kit contains. For these reasons, I recommend only the original equipment ATE repair kit. I have not looked at the NAPA kit (p/N 670) that has been mentioned in the newsletter as working but I suspect it has similar deficiencies. The Girling repair kit at my local Beck-Arnley distributor is quite complete except for all the important plastic bushing. The master cylinder can be disassembled sometimes by pushing in the piston and releasing it quickly, but this may not work, especially on the older ones. Then the bushing needs to be drilled out with a small drill bit.

Ed Note; I heat up the two small ring-shank nails and melt them into the plastic and then pull with two pairs of pliers. If you drill, take care not to score the piston with the chuck of the drill motor

One last word on brake master cylinders is that at least on the ATE ones ('71-on), one seal on the primary piston (I think) is nearly impossible to install on the new or old piston without breaking it. It can be done very carefully with small screwdrivers/fingers, but it is no fun. The problem is that it has to go over two rather high ridges on the piston. VW makes some cone shaped seal installing tools for their master cylinders, but none of them will fit the SAAB pistons--either too smaller too large. All this goes to say that you are best off keeping your brake fluid clean (flush/bleed at least every 30,000 miles) and when the master cylinder starts leaking, just save yourself some agony and buy a complete new one, though they are not cheap.

A replacement for the SAAB brake hose that goes from the wheel well to the front brake caliper on V-4's is available from Beck-Arnley. These hoses crack after 75,000 miles or less and should be replaced before the break works its way through the inside lining of the hose. The SAAB P/N 73-952-54 is close to $20 now and this universal type hose from B-A (P/N 073-0143) is only about $10.