AN114

OIL-INJECTION TO PRE-MIX CONVERSION

Can a two-stroke engine with oil resivoir and pump system be safely lubricated by putting the oil in the gas tank instead?

Ed Reply: I don't see any reason why you could not change an oil injected over to an oil-in-gas arrangement. Just bolt down a plate to the oil pump hole in the block with a gasket for a good seal. You'll want to add some oil through that hole every once in a while to keep the distributor drive gear from going dry since there's no source of oil there now, and no grease fitting like in the oil mix blocks. The oil pump normally pumps a small amount into the this front chamber with the distributor drive gear , so have to make up for that somehow.