AN115

OIL-INJECTION TO PRE-MIX CONVERSION

In response to the question in June '81 newsletter asking about the possibility of eliminating the oil pump on an oil injected two-stroke; I would not recommend it, as the main bearings have a plate next to them which guides the oil through them and a slinger which feeds the rod bearings under centrifugal force. The problem is this: the plate is right against the bearing; there is no way that the oil and gas mixture is going to lubricate the main bearings. The reason the main bearings last longer in an oil injector engine is the oil is not diluted with the gasoline. You get better lubrication with less than half the oil. The main bearings which would suffer from the loss of oil pump, but that's enough.

The oil injected two-stroke engine is a fine piece of machinery. I have two Sonett II and a Quantum III, all with oil injection--the only way to go with a two-stroke.