AN126

WIPER MOTOR

Sonett III hoods need not be removed to clean seized wiper motors. A mirror and flashlight are essential. Loosen the retaining strap slightly and spraying silicone on the rubber shield of the strap will make removal and replacement easier. After cleaning, drilling, lubing, etc., hold the brushes back with a single strands of wire wrapped up around the bottom of the gear housing. Put the armatures in the housing cup and twist this assembly back into the gear housing. When almost seated, remove the brush retaining wires, replace the bolts and calibrate the motor for maximum RPM via the axial adjustment screws on top and fiddling with the brush leads. After this is accomplished, a few drops of form-a-gasket and a cable tie will secure and seal the wires. Then a gallon sized ziplock bag over the top and rubber band to secure. Minimal time is 1/2 hr.