AN130

TRANSMISSION MAINTENANCE TIPS

Beware of a half a thread of the rear pinion shaft nut holding it on, and the loosening of this nut is likely what causes ring and pinion failure. There is a newer style nut and lock ring for the pinion shaft available from SAAB which will keep the pinion shaft together. It is P/N 87-106-34 for the locking plate, and P/N 87-106-26 for the nut. The pinion nut uses a left-hand thread in case you've had trouble getting it off. When tightening the pinion nut during reassembly, use about 100-125 lbs. of torque.

The Sonett has a higher final drive ratio than the 96, but you can use a 96 transmission in a Sonett, if you change the top cover and side bracket (if a Sonett III). Always change the clutch shaft seal when the engine is out unless you know you have done it recently. This will prevent oiling up the clutch from transmission oil seeping through the seal. A one inch section of one inch ID steel pipe will lock the freewheel slider into the cup on the input shaft and prevent the freewheel from coming out.