AN132

WELDING SEAM RUST

I made an interesting find during a recent inspection of my Sonett underbody. It appears that prior to painting the chassis, caulk was applied to many of the spot weld seams, plugs and etc. I found many areas where the caulk had pulled away from the seams leaving fine cracks for moisture to penetrate. This of course causes rust to form on the bare steel behind the caulk. Where this cracking is found the old caulk should be removed and any discovered rust treated using your favorite method. Recaulking with a non-hardening compound and repainting are also recommended.

I firmly believe this to be a major step towards preventing serious underbody rust problems. I urge one and all to grab their trouble lights and jackstands and go take a look.