AN134

CLUTCH

Be on the lookout for rebuilt pressure plates. The last ones I tried using I found to have bent fingers and heavy heat wraps on the bolt downs. When you have the plate tight be sure to check that the throw plate is level and does not sit below the surface of the plate. If it does the throw out bearing will not release the plate and all that you will get is a knocking from the throw out bearing arm hitting the plate. Be sure to check your arm for wear. If the arm is too worn (where the throw out bearing inserts at the top) the throw out bearing hits the plate at an angle and can cause the plate to fail and you do the job all over again.

One last item. If your front discs are not releasing and your brakes are dragging or wearing too fast, it might well be your hoses to the calipers. The rubber breaks down and prevents the brake fluid from flowing back, thus the brake remains on. The outside might look okay, but it's the inside that counts on this one.