AN135

WATER PUMP REPLACEMENT

Having busted my knuckes once too often replacing a V-4 water pump, I wrote out the following step-by-step instructions for my son so he could do it himself on his '69 96. I pass it along for whatever use some shade tree mechanic like me might want to make of it.

1. Drain the radiator--if coolant is freash and clean, you can save    and reuse it, but my advise is to discard it.

2. Disconnect negative terminal of battery.

3. Unplug alternator--just the plug wires, not necessary to    disconnect the wires bolted on.

4. Remove the alternator and carefully set it aside with three    wires still attached.

5. Disconnect the two hoses at the back of the engine that connect    to the water distribution pipe, undoing the clamps closest to    the block.

6. Loosen the metal straps that binds the two pipes together and    disconnect the two hoses that go into the back of the water pump    housing by loosening the front clamps and prying the hose back    towards the rear.

7. Loosen the 5 bolts holding the water pump housing to the pump.    Three are easy, but the two closest the block seem impossible.    Use 10mm socket and whatever handles enable you to get in ( a    flexible, universal-joint type socket helps). Pull off the    housing by pulling gently toward the rear. If it does not come    easily, pry carefully with a srewdriver to avoid ruining the    gasket, if possible (probably not).

8. If it is necessary to make a new gasket for the cover, be sure    to cut the right shape. This is too nasty a job to have to do    it again after discovering that your home-made gasket blocks the    water flow through the upper hose.