AN136

STEERING COLUMN REPAIR

Gradual fore and aft movement of the steering wheel is a problem that can occur on 95's, 96's and 97's equipped with the collapsible steering column.  This annoying problem arises from a reduction of friction between the male and female elements of the column, resulting in one or more of the following:

A) Loss of turn signal self-cancelling

B) Loss of horn function OR horn blowing when the steering         wheel is turned

C) A pleasant grinding sound as the steering wheel rubs 	   against the run signal or windshield wiper switch cover(s)

If you've determined that this is a problem on your vehicle, one solution is to establish some clearance between the steering wheel and the covers as shown in the first illustration.  Check that the horn blows and the turn signals cancel.  If not you have an additional problem.

Next remove the underdash cover attached to the steering column (if you have one), then locate, drill, and insert cotter pin as shown in the second illustration.  For best results and maximum retention of the column's torsion and "shear" properties:

--use a sharp drill

--make only one pass

--use the smallest bit that will allow a light press fit of the cotter pin.