AN137

RADIATOR FAN, WINTER DISCONNECTION

Here in the North there is no reason for a fan in the winter so I put a shorter belt on my V-4 and bypass the fan.  You get a little better mileage, save wear on the fan bearing and because there is more "warp" around the alternator pulley the belt can be run very loose saving the water pump.  The fan need not be removed but should be prevented from turning with some wire or tape.

On Saab Club advice I bought a pair of Kleber mud and snow tires.  They are great on snow and dry roads, better than the Michelin's on the other end of the car.

For those who would like a parts car but have no place to put it, a 96 can be completely taken apart in two days.  Everything unbolts and a lot comes off in complete units.  Example:  the half axle brake caliper, brake rotor, tierod end, shock, lower A frame all come as a unit.  Also you can remove the entire dashboard as a unit.  The car is incredibly well designed and this is what makes it easy to take apart.