AN139

V-4 SOLEX REBUILD

I have become something of an expert on V-4 Solex carbs, having rebuilt about 10 of them.  I have driven my 95 for some time without an accelerator pump, and there seems to be a slight improvement in gas mileage with no noticeable sacrifice in performance (?) at 180,000 miles.  What I have done is simply to remove the linkage between the throttle shaft and the pump lever and run a piece of wire into the instrument panel to activate the pump (a hood control or a manual choke would be better for this purpose).  I activate the accelerator pump only when starting the engine cold, to inject a small quantity of gas.  I now have very easy starting on the first crank (depress the pedal once only to engage the automatic choke, if you still have one), jerk the wire twice, and off you go.

I have also found that the so-called "Econostat" a vacuum-operated power booster circuit, has a pipe which tends to fall off from its press fit into the float chamber cover.  This once jammed the float all the way down, flooding gas all over the engine (no fire that time).  The fix is simply to press the pipe back in place, with Loctite 404 or equivalent; or you might simply remove it and plug the hole (perhaps removing the pipe in the venturi too, I haven't tried any of this).

I will confirm that  there was a safety recall on these Solex carbs due to the fuel inlet pipe (brass) popping off and causing a large number of burnt Saabs.  I received a recall notice which reached me in Berkeley in 1971 and I took the car to (then) Royce Motors.  They pulled on the pipe and it did not come out, so they said no need to fix.  Two years later, while doing a tune-up, it came out, so I reinstalled it with Loctite.  A much better fix was installed by Mecca Motors in Allston, MA.  A piece of bailing wire is attached to the two front cover screws and wrapped around the hose clamp on the inlet pipe.  This attachment should be secure.

When rebuilding the Solex, buy a can of any carb spray cleaner, such as Gumout. Be sure to check the float level on the car just after it has been running, unless you have the special gadget that screws into the float chamber (I have it,and have only used it once).  A rebuild kit for a VW carb with nearby Solex numbers will usually have at least the needle valve and seat and accelerator pump diaphragm.

After you have pulled everything apart, clean all jets and passages with the plastic tube inserted in the Gumout spray can.  Remove the plug or plugs sealing the pump check valves and gently remove the ball bearings (valves); clean thoroughly; replace the ball bearings and seat with a brass drift (gently).  Check operation of pump system before reassembling.  There is a small temperature compensating jet near the top of the pump chamber which allows a small quantity of fuel to escape back into the float chamber when the fuel in the pump expands due to increased temperatures.  If this jet falls out (you will find it when you remove the pump diaphragm) your pump will not work at all.

After your pump is rebuilt, and everything else cleaned out, put it all back together, being careful with the float chamber cover gasket.  Watch out for vacuum leaks near the passage to the automatic choke unloader.  when you put it back on the car, set the idle jet by hand to bottom out (gently) then back it off about 1 1/2 turns.  Warm up and check for gas leaks (none acceptable--watch particularly around the accelerator pump diaphragm and the jet access plug on the other side of the float bowl) and tighten (torque) the intake manifold if you haven't done so recently.  It is impossible to do a decent idle adjust if you have any vacuum leaks.  If your car is hunting (can't get a good idle setting) you probably have a vacuum leak.  Check your power brake booster if you have one, or else the above mentioned choke unloader, plus the induction manifold>.

(Ed. Note: To find vacuum leaks, spray carb cleaner on possible sources of leakage, like the base os the carb, throttle shaft, vacuum nipple, etc. If the engine speeds up when you spray the cleaner then you've found the vacuum leak.)

With car fully warmed up, follow factory procedure to set idle speed and mixture.  Set the mixture a hair richer than factors suggests-very lean operation might explain why number one exhaust valve burns?