AN14

SONETT EXHAUST SYSTEM

I found a good alternative to the Sonett exhaust system, sidepipes. I bought some pipes with built in mufflers, approximately 50" long and 3-1/2 " in diameter. Inlet pipe is done with 2" pipes, support was from some flat iron.

The pipes are angled so that the lowest point is behind the jack mount (so the car can be jacked up) and the highest point is at the rear with turn-outs. This reduced back pressure a lot, noise level is a deep low tone, and a little loud, but legal. If your Sonett is properly sound proofed, as mentioned in the Newsletter, the interior noise is livable.

A way to make your Sonett doors look better on the inside: I put an 8" tri axle speaker in each door, right before the hinges. To make your door visible at night, I took 2-door light/reflector combinations, with the light tied into the interior light and mounted them near the outer edge for visibility. Entry ia easier and safer at night.

For sound insulation in doors, white foam padding as in vinyl tops works good in the doors tight area where clearance is critical. For those who need more interior lights, a relay will help. A low power drain relay hooked in so when you open the doors, a ground will energize the relay and send a plus voltage to conventional lights.