AN147

CLOCK REPAIR

The VDO clocks one 95's and 96's often lost time or stop, but they are easily repaired.  Note that the round and square clocks are the same inside.  To fix your VDO clock you need to remove it from the dash and then take the three nuts off the white plastic cover.  The third nut is under the plastic seal (blue) a small cover for the nut to let factory repairmen know the unit hasn't been unsealed, you can just break it apart.  Once you have exposed the works, look for a massive flywheel-like part near the rear insulation board.  Remember when the clock worked it would tick for several minutes and then make a pop sound.  This is the part that makes the sound and it has one of a pair of electric contact points on it.  The proper closing of the points winds the clock by switching on an electromagnet momentarily and flipping the wheel.  The demon that stops these clocks is dirt on the points--just clean them up.

If this doesn't get the winding circuit running, the bad contact may have overloaded a fusible line at the far end of the magnet's copper coil.  The power comes in via a copper strip running inside the insulation board, the end of which is a tiny "O" -shape that attaches to the fusible link.  When the link melts the copper strip springs back flat on the insulation board.  To reconnect power, remove the bits of fusible metal and hook the copper "O" onto the tiny projection adjoining the bright metal tiny "O" that held the other end of the fusible link.  Now you've got a clock again, it only takes 15 minutes after the clock is out.