AN151

95/96 V-4 SURVEY

Thanks to everyone who responded to my request for owner input on the trials and triumphs of owning a V-4 powered 95/96.  In all, 38 owners wrote me and since only one had a 95 wagon, these results cover the 96 almost exclusively (though the two models are very much alike mechanically).

Mileage ranged from a low of 54,000 to an incredible 270,000.  The breakdown by model years was: '73--3; '72--7; '71--5; '70--8; '69--9; '68--3; and ''67--3.  Geographical response was wide, from Washington State to Bermuda and Texas to New York.  Since no one followed a pre-determined questionnaire, it would be unfair for me to list strong or weak areas as a percentage (for example, "60% reported a weak clutch" etc.)

I currently own a '73 96 with 80,000 miles and previously owned a new '79 900 EMS for two years in Alaska which I drove to my home here in North Caroling.  Let's start with the good points:

1). ENGINE: With the exception of valve jobs around 70,000 (avg.) the German powerplant is very reliable and sturdy.  Several people reported engines with well over 100,000 miles and no rebuilds.  Almost all "inferred" this might be the car's best point.

2). STURDY BODY 7 CONSTRUCTION: Most owners agreed if you kept up with corrosion and occasional leaks under your carpets, the little Saab was built like a brick out house, and would last virtually forever.  Older 96's should beware of windshield and floor pan crease seepage.  (Older 96's" now means all 96's I thin.  Ed.) Nothing a little sealer can't fix.  Accident survivability was also frequently mentioned.

3). UNIQUE DESIGN: What needs to be said? Nothing on the road looks like it, that's for sure.

4). HANDLING: Many praised the attributes of FWD and its firm, predictable handling.  My '73 is missing its front stabilizer bar and likes to lean in corners more than older 96's, but it is still a quick handler.

5). ECONOMY: All owners like the economy their 96's provide.  Average fuel consumption reported as high 20's for town and 30's on long trips.  The car is basically very economical also because it is so reliable and when things do go bad, the simplicity of the car allows owner performed maintenance much of the time.

Now for the bad or weak areas, (yes, even perfect people have vices):

1). TRANSMISSION: This is the number one gripe, without debate.  The proverbial weak link in an otherwise great car.  Most needed overhaul on average by 80,000 miles, some earlier, and a few are still going at 100,000 miles.  Mine has 80,000 and feels ok but like several owners commented, it "feels fragile." What tranny hints could I glean from all this?  To get lone life (80,000 to 100,000 miles): 1) use 75wt oil, 2) change it at least every 6,000 3) drive easy 4) lock out free-wheeling.

2). CARBS: There was lots of disagreement here.  The responses were divided 50-50 between Fomoco and Solex.  The Solex is difficult to work on, but better fuel economy and performance.  The Fomoco is simple, but not much else.  Aftermarket carbs were very popular.

3). BRITISH HYDRAULICS & WATER PUMP: There were many complaints on clutch and brake hydraulic parts.  The water pump is a real dog and replacing it every 50,000 miles isn't much fun.

4) EXHAUST SYSTEM: Many mentioned what they thought was early "burnout" with exhaust systems and the relatively high cost of replacement.  The MSS aftermarket system received a lot of praise for increased performance and longer life.  Exhaust system straps and hangers failed a lot, but I've noticed many good fixes in past Newsletters.

5). Finally, several people wrote to say they wished the Saab 96 had more power.  The car is a bit sluggish.  Granted it can cruise at 70 mph with no problem, it just takes a little time to get there.  Many said passing another car with a loaded 96 could prove exciting if not carefully planned.  You can add bits of power here and there with aftermarket carbs, headers, ignition and the like.  But before you bolt that turbo on your V-4, remember what kind of tranny is plugged into your engine. More power for the engine will probably mean less life for the transmission.

All who wrote loved their V-4's and would have another if available.  I've had mine six months and it is an economical, reliable little car, and good lookin' too.