AN154

BRAKES STICKING

I've been having some problems with the brakes on my '72 96. The pedal sticks down after each application of the brakes and has to be lifted back up with my toe. This will keep the brakes applied and the car stationary on a small incline. The problem is more noticeable in hot weather.

I have rebuilt the master cylinder, both calipers, and at least one of the rear cylinders. The spring on the pedal shaft is very strong and will send the pedal up when it is disconnected from the servo. I sure would appreciate it if you or one of the club members could be of help.

Ed Reply: Dragging brake problems in V-4 are often caused by flexible hoses to the front calipers. They deteriorate on the inside and block the return flow of brake fluid. The problem could also be in the vacuum servo (Sonetts do not have) which is between the pedal and the brake master.