AN155

WATER PUMP/ FRONT SEAL

The water pump bearing from older Toyota pickups will replace the V-4 fan bearing. Dimensions are identical except the Toyota has a longer shaft that must be ground off, but that's easy.

Also late model MOPAR oil filters are interchangeable with V-4 filters. The MOPAR filter is larger and usually costs about 1/2 the special imported filters.

Also found by accident, that there is a Honda (car) seal that will replace the balance shaft seal on the V-4 front cover. The accident was poking a hole in a new seal while installing it without the seal drive tool I had left at home. Not wanting to wait to have the $18.00 SAAB seal shipped to me, I checked out the seal board at my local Honda dealer and found exactly the same seal. I believe it is the crankshaft seal for a Honda. The cost is not quite $3.00 and it is a double wipe seal while the SAAB seal is only single wipe. The engine has run (it failed because the oil sending unit sprung a leak) for some time and shows no sign of leakage.