AN156

HIGH ALTITUDE TUNING

I. The factory recommends that the Mont Carlo and "S" engine be timed at 10 degrees before top dead center. For better performance at higher altitudes, you may advance the timing 1/2 degree for each 1,000 feet of altitude. We have found 12 to 13 degrees before top dead center to be an ideal setting for Denver - our altitude is being 5,000 feet plus above seal level.

II. Most of the "S" models that have arrived to date are equipped with 125 main jets which are too large even for sea level use.  These should be replaced with 120 main jets, if the car is not already equipped with 120's.

Main jet size 117.5 should be installed for altitudes of 2,500 feet and 115's should be installed for altitudes of 5,000 feet or over.

From the Saab Service Bulletin dated August, 1965:

"An improved design cylinder head has been introduced on all later 1965 standard model Saabs.  Because we do not have the information as to exactly when the changeover took place in production, we strongly suggest all standard models be checked.  The cylinder head is constructed so that the number 2 cylinder has a lower compression reading than that of numbers 1 and 3.  Number 1 and 3 cylinders have a compression reading of 125 psi + or - 7 psi. The number 2 cylinder has a compression reading of 115 psi + or - 7 psi.  The reason for this change was to reduce pinging that has been apparent in the standard engine.

When correcting an excessive pinging problem with the 1965 engine, a compression test should first be made to determine whether the improved design cylinder head has been installed on the car or not.  If the compression on number 2 cylinder is 10 psi + or - 7 psi lower than cylinders 1 and 3, the cylinder head need not be changed.  Should all cylinders read the same during the test, change the cylinder head to the improved type."

I can't help but believe that quite a few of these engines got through without the change being made.  It might be good to know BEFORE taking an engine apart.

In reference to your April article on Solex triple carbs not fitting pre-'64 two-strokes:  I had a local machine shop machine a one inch aluminum adapter plate in order to fit the Solex side-draft Sonett carbs to an older engine.  We went from the six-bolt pattern to an eight-bolt pattern and constructed three intake ports in the one inch plate to look like those on a newer model engine.  Works like a charm.  Had to allow enough room to adjust the distributor and cut the air cleaner down to fit under the Sonett hood.