AN157

V-4 SAME AS FORD INDUSTRIAL

As an "Oh, by the way" for Jeff Schille, the 91 cu. in. and 104 cu. in. Ford V-4 industrial engines are basically the same as Saab's version.  Notable differences are distributor curves, carburetor, water pump/fan assembly (with governor) and in some cases, the fuel pump is oriented differently.

The gasket sets are identical unless one has the silver engine ('67 & early '68) with 1/2" reach plugs.  There are other slight differences, but later model gaskets work fine (true of Ford or Saab).  If one has a front crunched 96 that needs a new front gear cover, Ford Power Products makes one without the snout and fan bearing assembly (almost half the price too).  for the savings, one can buy an electric fan and a smaller V-belt, adding economy and efficiency and no fan bearing to wear out.