AN158

RADIATOR FAN ELECTRICAL REPLACEMENT

For some time I've wanted to install an electric thermostatic-controlled fan on my '69 V-4.  A fan is sold out of the Whitney catalog for about $70 and it's dimensions are 13 3/4" by 3 1/2" deep.  My car is in storage back in the states, and when I measured the clearance between the radiator and the fan over the summer, there was only about 2 1/2" clearance.  so at that time I cancelled the idea.

But in the Feb. 1982 Newsletter on page two, Frank DeWitt tells how he shortened the fan belt to bypass the fan pulley altogether.  I've never removed any parts of the fan assembly, and I wonder if I could get the clearance by doing so.

Believe it or not, but after nine years with this Saab and many modifications to increase mileage I've gotten it to a true 41-plus mpg at 55 mph.  The MSS carb was good for 1 1/2 mpg, the air dam (Saab) upped it by another 2 mpg, and the use of slippery lubricants helped to the tune of about the same two mpg.  I'm just curious to see (I love to experiment!) how much I can get by eliminating the engine-driven fan.  Also, as Mr. DeWitt says, I would not have to worry about the fan bearing, though I haven't had to replace it yet in 145,000 miles.

I especially enjoy Jack Ashcraft's article on the V-4 and let me add my bit.  I think that many of the normal parts failures on the V-4 are due to simple abuse and lack of maintenance.  In 145,000 miles I've yet to replace a water pump, a clutch master, or have the pressure plate changed (my release bering is making noise now, so I'll have to have another soon.  Any only the rear brake hydraulics have been replaced (nothing on the front expect pads).  And the engine had only one valve job (at 50,000) and yet the compression is 160 plus on all cylinders now.

I replace oil and filters regularly, and I drive moderately, but not especially slowly, shifting with care (I use freewheel all the time).  Maybe I just got a car that was screwed together right, but I still think that many Saab owners punish their cars to keep up with the rally-car image of toughness.