AN163

OVERHEAD FAN SHAFT

Since most Club members who have 99's and 900's have never seen the engine layout of the pre-1965 two-strokes, I thought I would reproduce this illustration from the Saab factory service manual.  Actually the first Saab engine compartment I ever saw was an overhead fan shaft 96 that Herb Hewey had in Norman, OK back around 1974 or '75.  Since that was the first 96 engine I've ever seen, I just assumed all 96's had the radiator behind the engine.

So when Mark Welden and I picked up my first Saab, a dead '65 Monte Carlo 850, I was a little disappointed to see that it had the radiator up front, in the "conventional" position.  That is if you can call anything about a three-cylinder, two-stroke, fwd car with column-mounted gear shift "conventional."

While the overhead fan shaft design did have it's advantages--the whole hood and front grill were one piece and tilted forward for easy access to the distributor-the cooling system with its water pump siamesed to the back of the generator was inadequate in hot, non-Swedish weather.  Another problem was with the distributor right up front behind the grille, wet weather could make the "snub-nosed" 96's act like Lucas-equipped British cars.

But my '65 MC850 has never had any problems with wet weather with the distributor safely shielded by the radiator, and the cooling system is adequate for a hot August move to Minnesota, packed to the roof with all my worldly goods.  Or at least one Saab's worth of them.  The temperature did climb a bit on the grade up to the Allegheny tunnel in Pennsylvania, but the long freewheel down the other side cooled the engine down just fine.

Old Saabers insist that the pre-'65 snub-nosed 96's handle better than the later long-nosed versions, and the extra weight out front probably does affect the handling a bit.  But the move of the radiator forward corrected problems that were inhibiting wider sales appeal of the 96 and also set the stage for converting to the V-4 engine.  So the change to the long nose 96 is either progress or the beginning of the end, depending on one's point of view.