AN166

ENGINE HOW TO TELL DIFFERENT MODELS

Sales of two-stroke SAAB automobiles in this country spanned a period from 1956-1968. During that period a total of 10 different engines were used, but of these several have been replaced so that only a few are of current interest. The following is a list of these engines giving their usage and identifying characteristics.

STANDARD 750 CC 1956-1960

Look for a single carburetor, overhead fan shaft, water pump on the generator, and an eight bolt head. Uses crankshaft # 7828007, complete engine replaced by 1961-1964 standard 850 cc # 7819998. Recommended spark plug is a Champion UK-10.

GT-750 CC 1959-1962  [7828999]

Look for a single carburetor, overhead fan shaft, water pump on the generator, eight head bolts and a red block. Original crankshaft replaced by # 7828007, complete engine replaced by 1961-1964 standard 850 cc # 7819998. Recommended plug is Bosch MGV 260 T 31S.

STANDARD 850 CC 1961-1964   [7819998]

Look for water pump on generator, single carburetor, over head fan shaft, and 12 head bolts. Uses crankshaft # 7828007. Recommended plug is Champion UK-10.

GT-850 CC 1963-1964  [7835705]

Look for triple carburetor, oil injection, red block, and water pump on the generator. Uses crankshaft # 7829807. Recommended plug is Bosch MGV 260 T 31S.

STANDARD 850 CC 1965 ONLY  [7837453]

Look for single carburetor, water pump on the front of the head. Uses crankshaft # 7828007. Recommended plug is the Champion K-9.

MONTE CARLO 850 CC 1965-OBSOLETE

Look for triple carburetor with common throttle shaft, red block, and water pump on front of head. The intake manifold and carburetors are the only significant differences from the later 1966 and 1967 Monte Carlo engines. Uses crankshaft # 7829807 and recommended plug is Bosch MGV 260 T 31S.

STANDARD 850 CC 1966-1967  [7846801]

Look for triple carburetor, water pump on front of head. Uses crankshaft # 7828007. Recommended plug is Champion K-9.

850 CC SEPARATE LUBE 1967  also known as 850LD

look for triple carburetor, oil injection, water pump on front of head, green block. This is a standard tune engine with oil injection. Uses crankshaft # 7848724 with Monte Carlo pistons and rings. The tapered O-ring retainer on the nose of the crankshaft is not available as a spare part and should not be removed from the crankshaft. Recommended plug is Champion K-9.

MONTE CARLO 850 CC 1966-1967  [7847338]

Look for triple carburetor, oil injection pump on left side of engine and a red block. Uses crankshaft # 7829807. Recommended plug is Bosch MGV 260 T 31S.

STANDARD 820 CC 1968  [7867880]

Look for triple carburetor, standard engine, debored to meet emissions regulations. Pistons for this engine are not available, standard 850 cc pistons may be legally fitted by boring the block. These engines are identified by a yellow circle of paint on the rear of the block beneath the head. Uses crankshaft # 7828007. Recommended plug is Champion K-9.

NOTE all GT or Monte Carlo engines are painted red and must use Bosch MGV 260 T 31S plugs to prevent burning of pistons. Standard engines are generally green except for 1964 and earlier where colored varied from year to year.