AN171

ENGINE IDENTIFICATION # FOR V-4'S

My 96 is a 1971 model # 96607053. The engine from my old 96 1498cc is # 151506. I have a spare engine a 1698cc that is # 182654. Can some member tell me certainly where these engines were made, whether in Germany by Ford or in Sweden by SAAB, and perhaps when this switch was made?

Secondly, can someone tell me whether the cylinder heads can be successfully switched between these two different engines? The bore is the same, 90mm, only the stroke differ to alter the displacement, yet the two heads require different spark plugs.

Finally, my transmission has two numbers, one on top of the clutch bellhousing, F01342 and one cast directly in the ribbed case, 1483345. Can someone tell me what these numbers denote?

Ed Reply: I thought all the V-4 engines were made in Germany by Ford. If this is incorrect, perhaps someone else has the right information.

The cylinder heads for the closed-deck (blue and black) engines are interchangeable. The early '67 and '68 silver V-4 engines had an open-deck design (water jacket entirely surrounding the cylinder) and these heads cannot be interchanged with the blue (1500) and black (1700) engines. The silver open-deck uses short, 1/2" reach spark plugs while both the blue and black engines use 3/4" reach spark plugs. One way to tell the difference when looking at an unpainted head, is that the open-deck (silver) engine head has the center head bolt that goes through the exhaust hole counter sunk. Both the blue and black engines do not have this bolt head counter sunk.

The numbers on the top of the bellhousing is the serial number for the transmission. The cast in number on the case (and one on the bellhousing) is the part number.