AN172

V-4 TURBO

Turbo number three is on the road. Although I originally installed the turbo for performance, a real side benefit has surfaced; better gas mileage. Hard road mileage is 29 mpg and a steady 55 mph driving produces 38 mpg. I haven't ever achieved that on a normal aspirated SAAB yet. I think the Datsun carburetor that I am using has a lot to do with the increase. The carb is quite sophisticated and the vacuum operated secondary barrel seems to give much better mileage than either a single barrel or the Holley-Weber which has a mechanical secondary. I plan to install a Datsun carb on my two barrel SAAB, replacing a Holley-Weber and check it out.

I added a hood scoop which makes a big difference also. The engine was slightly rich and now runs slightly lean due to the cold (dense) air. I believe that any car can benefit from cool air as underhood temperatures can be extremely high, especially in the summer.

I plan to replace the scoop with a "NACA" vent as used on racecars and the 280ZX Turbo. They are more efficient than scoops and are available from the Datsun dealer or a race car supplier.

I finally found a place to have a hood louvered. A friend had his Volvo louvered and it really does help. I case anyone is interested, contact Bob "Gump" Andrews in Lewisberg, Ohio (513)-884-7339. He charges $.25 per louver which is a 1950 prices.

Some readers might be interested in some other sources of goodies that I have located:

: The trac Ignition, the one that lets you adjust the timing        on the dash and tune to the gas available, comes from: J&S        Electronics, 13925 Parkway Drive, Garden Grove, CA. 92643.        (714) 534-6975. They also make a very good water injection        unit and a Trac II turbo control unit.

: If you want to turbo a car yourself (I've done three now-       -it's easy), then check with : Shelby-Spearco, 10936 South        La Cienega Blvd. Inglewood, CA 90304, (213) 469-4860. They        sell the RHO-5 Japanese unit with a built in waste gate        which make for a clean, easy installation. They are experts        at sizing turbos to engines and can also give much valuable        advice. For a 1500cc V-4 they recommend The P13 housing that        I am using and I will vouch for its performance.