AN173

VALVE STEMS

For those with a V-4 that are using oil and pumping dark smoke out the exhaust (especially when starting then engine) the problem is probably valve stem seals. Do a compression check to ensure it isn't rings, just the same. Replacement of the seals is easy if you have a way to hold the valves in place while replacing the seals (rocker arm assembly  must be removed). The manual calls for a tool that sticks into the compression chamber, preventing the valve from falling down on the piston. I used an air hose fitting screwed into the spark plug hole; air pressure then kept the valves in place while I rooted out the hardened, broken remains of the old  seals. Easy, and no more smoke or oil consumption.