AN175

TRANSMISSION LEAKS/BUSHINGS

I have helped cure two recent cases of V-4 transmission oil leakage that could not be cured by new seals, regluing the bellhousing or any of the usual fixes. The problem turned out to be, in both cases, a badly worn pilot bushing in the flywheel (or more accurately, the crankshaft).

What happens is that when the pilot bushing is worn, it allows the clutch shaft to wobble in an elliptical path. This wobble pushes out the lips of the clutch shaft seal in the bellhousing (no matter how new the seal may be), and lets tranny oil by the seal into the clutch area.

I now check the pilot bushing on all V-4's when the entire engine is out for a clutch job, or any other repairs. The pilot bushing only costs about $1.85 from SAAB and is cheap and easy to fix when the engine is out of the car.

To remove the old bushing, just chisel out a small section of the bushing with a small cold chisel and the rest of the bearing will come out easily. Drive the new bushing in with an old clutch shaft or a plates clutch alignment tool should work also. The diameter of the end of the clutch shaft fits into the pilot bushing is 19/32" if you want to check it for wear. I just check the wear with the clutch shaft itself by wiggling it in the bearing.

Smear a little grease in the pilot bushing before you put it back in to help prolong its life.

Faulty Clutch Disc:: Many people get to do a second V-4 engine R & R on their 95/96/97's because of a new clutch disc that was bad. The linings halves of the disc were sprung wider apart atone part of the disc's circumference which caused the disc to drag on the flywheel and pressure plate even with clutch at full travel.

This "bulge" in the clutch disc does not reveal itself in the normal check for shimming the pressure plate. (this is where you put a straight  edge across the pressure plate with disc and plate bolted up to the flywheel. If the triangular plate that the release bearing presses on is more than 1/16" below the straight edge, you need to put some washers under the pressure plate bolts, between the plate and flywheel.

To check for "bulges" in the disc, just measure the thickness of the disc at several points around the disc and make sure it has roughly the same thickness all the way around.