AN179

BALANCE SHAFT GEAR FAILURE

V-4 Balance Shaft Gear-- On my last trip from Vermont to Minnesota, my 1971 96 left me in a fix in Michigan City, Indiana, when the fiber gear on the balance shaft failed, after 11 years of service.  The problems is easy to diagnose (the motor runs, but the fanbelt doesn't move), but it is no fun to fix.  My solution was to tow the car home (500 miles), remove the engine, take off the front cover and oil pan, and replace the gear.  I was lucky to get an all steel replacement, used, at an industrial Ford dealer here for $25.  I was not happy, though, to discover a broken tooth on the camshaft gear.  There is not steel replacement for this one, and the new fiber gear cost $94.50 at Ford.  (I also got a front cover seal there for $4.50 as compared to $24 quoted by a local dealer.)  The whole project, including the cost of towing the car back, cost me about $450.00.

This is the second time I have been stranded in a Saab, due to failure of the balance shaft gear.  The first time was in the summer in Missouri, also en route to Minneapolis.  It was a motor which had been driving an air conditioner for most of its life, and it failed at 84,000 miles.  This time the motor had much higher mileage, but had never driven an air conditioner, nor had the fanbelt ever been unduly taut, or the fan, alternator or water pump bering faulty.  I can only assume that this fiber gear represents a true "weak link" in the V-4 motor, in the sense that other parts of the motor are not subject to structural failure due to stress/concentrations, or fatigue, and accordingly their useful life is determined by the nature of their use and the processes of normal wear.

It would seem prudent to recommend that members consider the replacement of this gear as a routine maintenance procedure sometime after 75,00 miles, perhaps while the engine is already out of the car for clutch replacement or gearbox overhaul.  It will not be possible to replace the gear without removing the engine, so it is not just as well to buy the replacement part and keep it in the glove box.  If the fiber hear is replaced with the all steel unit, it will never have to be done gain.

As regards the camshaft gear, I can only imagine that mine failed because of unusual stress after the balance failed . The camshaft gear is twice as large, with much better mechanical advantage, and much more uniform loading.  I do not believe this gear will fail as a matter of course.

Ed. Note: The steel replacement gear for the V-4 balance shaft is no longer available.  Pat Lawrence of Motor Sport Service advises that they plan to get an estimate for having a quantity of the gears specially made, but this may be awhile.  There may still be

AN179

some used or even new gears available at industrial Ford dealers, but one such dealer I contacted reported that the gear was "discontinued."

There are some warning signs of incipient balance gear failure.  One is a noticeable "whirring" sound on deceleration caused by excessive back-lash of the worn fiber gear.  The fiber gear was used by Ford instead of the longer lived steel unit, because it is somewhat smoother and quieter.  And at an average life of about 125,000 miles, the fiber balance gear only seems a "weak link" in an engine as rugged as the V-4.