AN18

V-4 INSULATE BARE WIRE IN STARTER

My starter refused to turn the engine over despite a good battery and connections. The local dealer insisted that I need a new starter. Not convinced , I removed the starter and discovered the problem to be a shorted lead. It seemed that on Bosch starter, the battery power first goes to the solenoid, then via a bare lead, thru a hole in the starter to the brushes. Repair cost about was some electricians tape to insulate the lead. Originally there was a rubber grommet at the hole, but it had long ago rotted away. Tape it up when you have the starter off for other repairs.