AN180

34 ICH CARB

I have traveled nearly 5,000 miles now, under many different driving conditions, with the new Weber 34-ICH carburetor in my '71 96 and I am ready to recommend it without qualifications for any 95/96 owner, I am using a 1500 cc motor (from a '70) but I believe the carb will perform as well with the 1700 cc motor. This carburetor is incomparably better than any of the Solex or Ford models originally fitted. My car now starts instantly, cold or hot, idles smoothly, and accelerates very nicely, though it is not quite as fast as with a good Weber two barrel. Driveability is excellent and gas mileage is the best I've seen for a V-4, I'm getting 23 to 26 in Minneapolis and 32 to 36 on the highway (these are real mpg figures, after correction for odometer error).

Installation was a little more tedious than I had expected the main difficulties involving the fitting of the air cleaner and PVC valve 9the valve as it exists, will not fit under the new choke linkage). The throttle linkage was not a problem. I simply removed the throttle lever and replaced it with the comparable part from the old FOMOCO carb (it fit without alteration) and I used the standard linkage without any modification, Of course the standard linkage was never a very elegant affair, and almost any modification made at this point should be an improvement.

The carburetor features a manual choke, which suites my preference in this cold climate, and it also has a solenoid idle cut off, which might be helpful if you are having trouble with dieseling or after run. My carb runs slightly richer than the Ford, but it is well within the correct range, as evidence by its optimal performance.