AN181

CARB WEBER 34 ICH & PVC CLEARANCE

I installed one of the Weber 34-ICH carbs on my '70 96 and when I inserted the PVC valve in the intermediate plate, it came right up to the choke lever and obstructed the choke linkage, thus preventing movement from the control on the steering column.

To clear the PVC valve away from the carb, I shopped for two small brass fittings, a short union (connector) and a 45 degree elbow. These were mounted in the intermediate plate. At the other end of the elbow (directly away from the carb) I now attached the PVC valve. This was followed by attaching the original curved rubber hose to the PVC valve and the valve cover. Everything fits well under the air cleaner.

No there are no oil deposits in the air cleaner as there were when I had the PVC valve disconnected. Tentative testing indicates about 23-24 mpg in local urban driving.