AN188

PILOT BUSHING REMOVAL TOOL V-4

That was a good tip on the flywheel bushing, something I'd never thought of as causing a transmission seal to leak.  I have removed pilot bushings in the past by filling the hold with grease, then driving in a clutch shaft or tight fitting drift.  The resultant pressure on the grease forces the bushing out.  I think the Haynes Manual suggests this method.  It may work no better than a chisel, but it is more fun.

Bleeding clutch hydraulics--For the last five years or so I've been bleeding late V-4 and 99 clutches with a spare cap.  I drilled an appropriate sized hole in it and installed a Schraeder-type tire valve from a Michelin bicycle tube.  It has a threaded stem and a nut to lock it on the tube which simplifies attaching it to the cap. A standard rubber valve stem for a tubeless steel rim might work as well.  I use a hand pump--compressors blow them apart.