AN193

CHANGING FRONT HOSES

I would like to help solve Willard Freedman's problem with 95/96/97 front brake hoses.  First remember the steel lines may be weak at the union, so don't twist it!  I've used a tubing wrench ("flare nut wrench") that is like a slotted box wrench, to fit over the line on the inside, but watch that twisting.  If your steel line is stuck to the compression nut itself and twisting, stop!

If the flexible hose is bad, but it; if good, loosen at the caliper then remove the caliper and unscrew the caliper from the hose.  Now with the tubing wrench inside, or a vise-grip, use another vise-grip or small pipe wrench on the top metal end of the flex hose.  The hose itself is held onto the wheelhouse anchor, but will usually turn out enough to allow you to turn out the inner compression nut without breaking the steel line.  Penetration fluid long before you have to do the job helps.

I constantly recommend that owner/repairers always have a pump oil can (or WE-40 or similar) at the ready whenever they jack up their cars.  Putting a drop of oil on these connections, on bushings, nuts, bolts, body seams, hinges, brake caliper pivots, handbrake cables, rear brake adjusters, wiper arms, etc., can save hours, dollars, and aggravation.