AN197

SONETT ROCKER PANEL RUST REPAIR

In answer to Chuck Repede, when my '72 Sonett rocker panels rusted, I elected a temporary repair.  I covered the old rocker panels with aluminum rocker panels that I cut from sections of rain gutter and pop riveted them in place.  It makes a fairly decent looking repair at minimal cost.  It turned out to be the right choice, because it was only one more winter before the frame rusted through at the lower A-arm.

If Chuck wants to do it right, I recommend Autographics in Painesville, OH.  They replaced both rocker panels on my '73 Sonett and repaired some rust-through in the floor and trunk for about $400, a good price.  I waited months for rocker panels from Saab, but Autographics said they could fabricate them for about the same price.

Regarding Zinc Galvanized steel for rust repair:

A small alarm went off in my head when I read about welding galvanized steel in this Newsletter and the NE Sonett Club Newsletter.  I checked it out with a metallurgist friend and confirmed that:

1. The fumes from welding zinc are toxic.

2. The zinc contaminates the weld and makes it weaker.

It is better to stick with plain steel.  Jack Lawrence recommends a self-healing zinc primer, and named Sherwin-Williams as one supplier.