AN198

INSTALLING V-4 POWER TRAIN

If you are one of the die-hards who always drop the engine and transmission back into the car in one unit, you can make installation easier by disconnecting the wheel hub and pulling the axle out a bit.  You just back off the two bolts (with locking tabs) which hold the steering arm to the hub (leaving top ball joint on the A-arm) and pull the hub/brake disc down.  This pulls the axle out, giving you more room to mate up the axles and inner drivers of the transmission while all that weight is hanging in the air.  The service manuals suggest this for the 99, but it works just as well on the V-4 too.