AN199

CARB SOLEX CURING HESITATION

I've been running my V-4 Sonett in Solo events now for a couple of years and the only pig problem has been a hesitation when making hard right turns, especially those following braking.  The cause was evidently that the fuel was being thrown away from the main jet area of the float bowl.

Normally, raising the float level will cure this.  But raising the float level on the Solex carb normally results in the float hitting the bowl vent boss in the carb top.  However, if you grind away part of the boss (stop before getting into the vent passage) you can raise the float level significantly.

I did this and the hesitation has not occurred in the two events I've run since making this change.  The car also seems to pull stronger from low rpm than it did before with none of the slight hesitation I sometimes felt.