AN2

ANOTHER WAY TO WORK ON THE V-4 CLUTCH

First of all, the problem is not always the travel of the release fingers, but the thickness of the clutch disc. This bit of information comes from R & R of my V-4 four different times, for the same clutch job.

Upon replacing the big three in my V-4, it would not release. We then shimed the slave cylinder to the point where the clutch pedal would no longer go all the way to the floor and the fingers were making a racket as they hit the disc and/or flywheel. And so it went as we investigated the problem for the next two R & R's to make it short, the best way to perform the operation is as follows once the engine is out.

1. Measure the distance from the flywheel to the top of the fingers of the old assembly.

2. Bolt up the new assembly and measure the same. If these distances are nearly equal(usually about 3.2 cm) the job will more than likely go as smoothly as normal. If the distance is varied too much 4.8 cm approximately, shim the pressure plate until the distances are equal. If they were equal to begin with, it may be necessary to shim the slave cylinder, but probably not.

I hope this will save the members some time and trouble, like 4 to 8 hours and some blood that I gave for my experience. By the way, this problem has come about by SAAB changing suppliers and therefore changed the thickness of the disc and jobber parts, also vary in thickness from original. The thickness will not affect all V-4's the same however, that is why I recommend the measurement system.