AN200R

SONETT HOOD LATCHES

The rubber hood latches on my plastic wonder car once again fell victim to the ravages of sun, ozone, smog, and old age, and had to be replaced.  They are an abominable piece of design in the first place--I mean who in their right mind would attempt to secure the entire front end of a car with a rubber band?  And to add insult to injury, Saab seems to think they should be worth something like $40.  Not to me they ain't.

A tour of the local VW off-road parts house turned up a set, distributed by some Southern California outfit called Bug Pak(part no. 6028) that retails for $6.  Now thats more like it.

The new latches are about 3/4" shorter than the originals, but if you take out the two bottom screws of the mount bracket and rotate it 180 degrees about the top screw, then drill holes and install the two screws in the new holes, it fits just fine.  I put a pair of pan head screws in the old holes with a bit of silicon seal under the heads, touched them up with some paint, and the job is done, at a saving of about 35 bucks in the process.