AN203

SPEEDO SURGE AND PINION

Robert Allen asked why a V-4 speedometer "surges" and "drops back" on freewheel.  I had such a problem which a mechanic corrected in connection with some other work.  The speedometer drive gear is sandwiched between the third- and fourth-speed gears on the pinion shaft of the transmission.  When the nut on the back of this shaft loosens, the speedometer drive gear can slip, and presumably does so when power is not applied to fourth gear.  Tightening the pinion shaft nut fixed the surging speedometer in my car.

Another curious speedometer problem occurs only in extremely cold weather.  At higher speeds the reading becomes unrealistically high, even pegging at 100+ mph at a true speed of 50-60.  Usually there is some noise also.  This problem goes away when the temperature rises to ) degrees F.  I believe it may be due to frost crystals inside the speedometer, but it may also be a frozen lubricant inside the speedometer cable which makes the center, or "drive" part of the cable, act like a spring, momentarily slowing at the speedometer end, then breaking loose and suddenly revolving at very high speed to catch up.  For this to be correct the speedometer must notice the fast motion and ignore the slow.  Unfortunately the manuals do not describe the speedometer's construction.

A third difficulty I have had was a sort of ticking noise at all temperatures, with vibration of the needle +/- 1 or 2 mph.  The noise became worse until, with a loud snap, the speedometer quit somewhere in New Mexico.  The cable was intact but the connector inside the speedometer had snapped.  Luckily I had time to locate the only 1968-69 speedometer in all of El Paso's junkyard.  Later I was advised to squirt some oil into the speedometer at that cable connection.  This is best done by removing it from the dash.

Rebuilding 95 Rear Shocks?--As the operator of a "fleet" of three 95's, I would like to learn of anyone who can repair the deals on the rear shock absorbers (lever action).  I have a small collection of leaky and perhaps worn ones--they cost a fortune.

Ed. Note: Performance Cars lists a rebuilt 95 rear shock for $61.55 exchange.  Their address is 9916 Jefferson Ave., Newport News, VA  23605.

Broken Upper A-Arm--David Roth's broken 99 A-arm intrigues me as I recently had a similar failure, except that it was on a 1969 95 that has gone 170,000 miles.  I don't know about fatigue, but in my case the crack had begun earlier since the beginning of the split was rusty.  It may have come from a particularly nasty pothole that I hit several months earlier.  Luckily when the A-arm did break it was at about 3 mph at a stop sign; one mile further on the freeway and it is hard to see how I could have avoided a spectacular crash.