AN204

MORE SPEEDOMETER SURGE

Speedometer surge in the V-4 (and 3 cyl.) transmissions may have one of two causes:

1) The carrier for the nylon speedo driven gear may be loose.  Simply tighten with a large crescent wrench, being mindful of aluminum threads.

2) The large nuts which position the three shafts in the gearbox may have loosened, allowing end float of the shaft(s).  This is more serious, as the nuts will continue to back off until they literally mill through the rear cover of the gearbox.  Unfortunately, the only fix is to pull the trans' and retorque the nuts.  THis, however, is easy compared with the repair job that awaits if the nuts do cut through the cover.