AN207

REAR BRAKE JOB

Rear brakes--I did a rear brake job on a 96 last week and found one wheel cylinder frozen, the other leaking.  People should change their brake fluid more frequently.  I noticed I was doing some things other members might like to know.

Before pulling the drums off, back off the adjusting screw so the brake shoes do not drag on the drum.  If you replace the shoes, back off the adjuster completely before reinstalling the drums.  After you've adjusted at the backing plate, adjust the handbrake to take up the slack--the two systems work together and doing this will take up the slack in the mechanical part of the system.

When putting on a new wheel cylinder, I find it is quicker to remove the bleed screw and spin the cylinder onto the compression nut on the line, rather than to turn the nut into the cylinder. When it is almost tight, I install it in the backing plate, putting the bleed screw and split pin through their respective holes, then tightening the nut with a wrench.  Take care when turning the nut--it is easy to twist the brake lines.

When installing a new grease seal in the brake drum, I lay the seal face down on the bench and push the drum onto it, instead of trying to drive the seal into the drum.  Much easier.