AN209

FREE-WHEEL REBUILDING

I recently dealt with my first late-style 96 freewheel, complete with ten rollers, 20 plungers and 20 springs.  I've mastered the assembly of the older six roller style with my bare hands, but this required a different approach.  I ended up putting a dab of grease behind each roller to hold it and the corresponding pair of springs and plungers in place, until I could twist the unit with an input shaft and tighter a wire round the rollers to retract them for installation.  I rinsed the assembly in solvent to remove the grease before putting it in.

Some people might not know about using apiece of tubing, such as brake or fuel line to hold down the detent balls while putting the shift rails into the shift forks.  The hollow end of the tubing holds the ball depressed securely until the tip of the rail reaches.  I do one shift fork at a time, and shift the forks rearward, rather than move the rails forward.

As long as we're onto transmissions, I would like to remind members to regularly change your tranny oil.  If you can only get a pint out, or you get a heavy smear of silver "mud" in the drain pan, you've waited too long.  It's much cheaper to maintain a Saab transmission than it is to repair one.