AN210

CARB SOLEX FLOAT CURES

My article in the previous newsletter described a cure for a right-turn stumble in a Solex carb for a V-4. This involved grinding away part of the bowl vent so the float could be raised, since the cause of stumble was fuel starvation due to the fuel being thrown away from the main jet. This has proved effective.

However, I now occasionally get the carb to flood when making left turns. This is caused, evidently, by the higher float level, and the cure is probably a "fine Tune" of the float level. This problem is most noticeable on very hot days and with a thoroughly warm engine, like when you make back to back autocross runs. I'm using a 160 degree thermostat which helps.