AN212

FAN BEARING V-4

The V-4 fan bearing is very expensive, but this is a common type of water pump bearing available from bearing stores for about $9.00. The trouble is, most have shafts that are too long and a hacksaw won't even scratch it; neither will a carbide lathe tool. The best solution is to find a bearing store that has New Departure #88P165 NDH. This one has one shaft end flush with the housing like SAAB's, and the other end less than 1" longer than SAAB's which is no trouble.

I removed the old bearing and installed the new one by heating the engine cover with a propane torch, but I found I still needed a slide hammer to get it out.