1AUXILLARY LIGHTS SONETT

AN215

AUXILIARY LIGHTS SONETT

This modification is easily accomplished by anyone who works on their own car and will improve the looks and night visibility of your Sonett III.

First go to the local junkyard and find a 1970-'71 Capri. This model has individual headlight buckets that are identical to the original SAAB auxiliary buckets. Later Capri's have a stamped steel bucket that houses two lights and cannot be used.

Remove the two inner buckets, leaving as much wire as possible so you won't have to splice wires later. Install the buckets in your Sonett using the nuts and bolts from the Capri. I think that the housings are designed so that they cannot be installed upside down. Connect the wires as shown, using a male connector for the hot wire, and splicing into the ground as shown (or run a separate ground). The male connectors can be purchased at any good auto parts store. They must have the same tang on them so that they lock into the canon plug. If you do not have a pair of electrical crimping pliers, get one. I have used all manner of pliers and the connections just will not last without the correct tool.

The SAAB factory wiring does the rest. With the main lights down, and the "AUX" switch on, the auxiliary lights will flash when you pull the dimmer switch. When the main lights are up, the auxiliary lights will go on with the high beams.